## Slide 1: VLSI System Design Final Project Demo
107065507 盧允凡

## Slide 2: Outline
RSA
First approach
Second approach
  FSM
  Block Diagram
  Cycles Analysis
  Simulations

## Slide 3: RSA Engine
KEY: E, D, and N
Input data: A
All 2048-bit
Using LR algorithm to compute A**E (mod N)

## Slide 4: First Approach
RTL simulation passed, but synthesis failed.
the multiplier is too big!!!
2048-bit x 2048-bit
Second Approach
Using word-based design to do the multiplication.
multiplication fixed, but modulo is still unsolved.
RTL simulation passed, but synthesis failed.

## Slide 5: LR algorithm

## Slide 6
IDLE
KEY_E
&
KEY_D
&
KEY_N
DATA_FEED
LR_1
LR_2_MUL
RELOAD
LR_3
LR_4_MUL
RELOAD
LR_4
OUTPUT
DONE
x64*3
x64
Find the msb
Word-based multi
Word-based multi
If statement in LR
FSM
x64
64x64
64x64
O(2048)
x64
x64

## Slide 7: Block Diagram
clk
rst_n
exe
addr
wen
data
mode
32
32
result
oe_n
filter
8
status
SRAM
32x256
testbench
done

## Slide 8: Word-based multiplication
Split 2048-bit into 64 x 32-bit.
require 64*64 cycles to complete the computation.

## Slide 9: Cycles Analysis
Input key: 3*64
N data feeding: N*64
LR algorithm: N*(O(2048)*64*64+64)
Output: N*64

## Slide 10: SRAM area estimation
The area of a single-port 32*256 SRAM is 43400 um2.

## Slide 11: Simulations
Example 1
Public key: (E, N) = (7, 143)
Message = 03 08 23 01 14 07

## Slide 12: Simulations
Example 1
Private key: (D, N) = (103, 143)
Message = 42 57 23 01 53 06

## Slide 13: Simulations
Example 2
(E, N) = (157, 2773)
Message = 948